## Slide 1
iver
The next generation stream design
https://riverarchitect.github.io
river.architect.program@gmail.com Davis, CA | 2019
rchitect

## Slide 2: Highlights
Introduction
Motivation
State-of-the-Art stream design involves subjective and individual approaches that sometimes miss their objectives (ecological abundance and long-living)
Methods
Parametric and transparent design concepts
Product
Ecologically sustainable and long-living fluvial landscapes with economic assessment
Source: Greg Pasternack @RiverSciLife
Source: S. Schwindt
Concept

## Slide 3: Highlights
Introduction
Lifespan & Design Mapping
Longevity assessments of single features
Morphology
Terrain modification to yield self-sustaining fluvial landscapes and mass movement assessments
Ecohydraulics
Habitat quality and connectivity assessment for target species and their lifestages
Project Maker
Presentation-ready wrap up of project costs and benefits
Modules

## Slide 4: Lifespan & Design Mapping.

## Slide 5: Lifespan mapping
River Architect
Methods
Source: Schwindt, S., Pasternack G. B., Bratovich, P. M., Rabone, G., Simodynes, D. , 2019. Hydro-morphological parameters generate lifespan maps for
stream restoration management. Journal of Environmental Management 232, 475-489. doi: 10.1016/j.jenvman.2018.11.010

## Slide 6: Lifespan mapping
Input
Flow data
Chart: Discharge (m³/s)
Chart: Return period (years)
| 50 | 40 | 30.030030030030026 | 20 | 14.999250037498127 | 10 | 5 | 2 | 1.1111111111111112
FLOW (10³ cfs) | 166.9535 | 147.5104 | 125.0124 | 97.4193 | 80.6861 | 60.5141 | 34.1042 | 11.4942 | 2.25

## Slide 7: Lifespan mapping
Input
Rasters
2D hydrodynamic modelling
(depth, velocity)
Digital
Elevation
Model
Grain sizes
Morphological Units (instream)
Detrended DEM
Depth to Groundwater
Chart: Return period (years)
| 50 | 40 | 30.030030030030026 | 20 | 14.999250037498127 | 10 | 5 | 2 | 1.1111111111111112
FLOW (10³ cfs) | 166.9535 | 147.5104 | 125.0124 | 97.4193 | 80.6861 | 60.5141 | 34.1042 | 11.4942 | 2.25

## Slide 8: Features
Introduction
Stream design feature groups
Parametrization: Survival threshold values
GROUP 1: Berm setback, calm water zones, grading, side channels, bank scalloping
GROUP 2: Vegetation plantings &
other (soil) bioengineering
GROUP 3 – Longitudinal connectivity: Sediment budget modification,
flow regulation, lateral barrier removal
(not yet fully considered in River Architect)
Parameter (unit) | Depth to ground water (m) | Dim.less bed shear stress (--) | Froude number (--) | Flow depth (m) | Flow velocity (m/s) | TCD: Fill (m/year) | TCD: Erosion (m/year)
Grading | 2 - 4 | 0.047 | na | na | na | na | 0.01
Etc. | … | … | … | … | … | … | …
Features

## Slide 9: Lifespan mapping
Methods
Sustainability Criteria – Thresholds
Source: https://github.com/RiverArchitect/program/blob/master/LifespanDesign/.templates/threshold_values.xlsx

## Slide 10: Lifespan mapping
Lifespan mapping
Calculous
Lifespan Calculation (Raster overlay)
Identify best lifespan within feature groups
Source: Schwindt, S., Pasternack G. B., Bratovich, P. M., Rabone, G., Simodynes, D. , 2019. Under preparation

## Slide 11: Lifespan mapping
Lifespan mapping
Example: Identify stable log diameters for streamwood placement
Design maps

## Slide 12: Lifespan mapping
Lifespan mapping
Result processing
Use for planning terraforming actions: Manual action required
Use for full-automated planning of vegetation plantings & other bioengineering features
And more …
… gravel augmentation
… streamwood
… mass movement
Results

## Slide 13: Morphology.

## Slide 14: Morphology
Morphology
Use Threshold-based terraforming or River Builder to design riverscapes
Threshold-based terraforming: Grading or River widening
River Builder
Volumetric Terraforming assessment
… these routines procedualize
currently best available science
… we are developing new strategies
to improve procedural terraforming
based on physical boundary conditions
Overview
Synthetic river valley created with River Builder
(source: Gregory B. Pasternack)

## Slide 15: Ecohydraulics.

## Slide 16: Ecohydraulics
Habitat
Define Fish
Habitat assessment (1): Habitat Suitability Index (HSI) of juv. Chinook salm.
Source: Schwindt, S., Pasternack G. B., Rabone, G., 2020. [submitted manuscript].
Chart: Probable habitat suitability (--)
| 0.2 | 0.55000000000000004 | 1.5 | 2.5 | 3.5 | 5 | 6 | 11.9
Depth HSC | 0 | 0.5 | 1 | 1 | 0.35 | 0.35 | 0.2 | 0
Velocity HSC | 1 | 1 | 0.99 | 0.98 | 0.97 | 0.96 | 0.94 | 0.92 | 0.89 | 0.87 | 0.84 | 0.81 | 0.78 | 0.74 | 0.71 | 0.67 | 0.63 | 0.6 | 0.56 | 0.52 | 0.48 | 0.45 | 0.41 | 0.38 | 0.34 | 0.31 | 0.3 | 0
DHSI (Depth)
VHSI (Velocity)
Combined HSI (cHSI) =

## Slide 17: Ecohydraulics : Habitat Enhancement
Habitat
Methods
Habitat assessment (2): composite Habitat Suitability Index (cHSI) map
Repeat operation for multiple discharges (apply flow duration curve)
Calculate usable habitat area (e.g., cHSI > θ = …)
Source: Schwindt, S., Pasternack G. B., Rabone, G., 2020. [submitted manuscript].
Usable Area

## Slide 18: Ecohydraulics: Habitat Enhancement
Fish preferences in River Architect
Usable habitat is where θ = …
Habitat
Define Fish

## Slide 19: Ecohydraulics: Habitat Enhancement
Habitat
Methods
Habitat assessment (2): composite Habitat Suitability Index (cHSI) map
Repeat operation for multiple discharges (apply flow duration curve)
Calculate usable habitat area (e.g., cHSI > θ = …)
Sum of usable areas for one discharge = SHArea
Sum of multiple season-specific discharges = Seasonal Habitat Area (SHArea)
Source: Schwindt, S., Pasternack G. B., Rabone, G., 2020. [submitted manuscript].
Usable HabitaArea

## Slide 20: Ecohydraulics: Habitat Enhancement
Habitat
Methods
Habitat assessment (3): Calculate Seasonal Habitat Area (SHArea)
More: https://riverarchitect.github.io/RA_wiki/SHArC#herunSHArea
… and season

## Slide 21: Project Maker (Cost-Benefit Analysis).

## Slide 22: Project Maker
Projekt Maker
Site-wise metrics
Automated terraforming assessment
Automated vegetation plant-ings & other bioengineering placement
Automated cost assessment
Input

## Slide 23: Project Maker
Projekt Maker
Output
… Project key metrics

## Slide 24: Highlights
download https://riverarchitect.github.io/
docu https://riverarchitect.github.io/RA_wiki/
maintenance S. Schwindt, K. Larrieu, G. Pasternack